## Slide 1: Fire Detection And Alarm System
Using PLC
PLC

## Slide 2: Table of Contents 01 02 03
Functions of the system and system description
Application Overview
Role of PLC in the application
How to represent this system using PLC
Ladder Diagram
Utilizing a ladder diagram to simulate the plc's operations

## Slide 3: Application Overview 01

## Slide 4: Purpose of the App
- Monitor and detect fire or smoke in real-time.
- Alert users immediately through alarms and notifications.
- Improve safety and reduce response time in emergencies.

## Slide 5: Increases Enables Works with
Quick action before fire spreads
safety and awareness
existing fire sensors and PLC systems

## Slide 6: Target Users
Shopping Malls
Airports
Hospitals
Homes
Schools and universities

## Slide 7: Role of PLC in the application 02

## Slide 8: Advantages of using PLC
Fast Response
Detects and reacts to fire quickly to trigger alarms and safety devices
High Accuracy
Reduces false alarms with precise sensor input handling
Easy Monitoring
Provides real-time status and alerts for immediate action
Scalability
Can be expanded to cover larger areas or additional zones
01
03
04
02

## Slide 9: System inputs
Start / Stop Button
Heat Sensor
Manual fire indicator
Smoke Detector
1
2
3
4
Allows manual activation or deactivation of the device
Enables fire alert if detectors haven't responded yet
Triggers alert when temperature exceeds threshold or increases rapidly
Detects smoke particles and triggers an alert in the presence of smoke

## Slide 10: System inputs: Heat Sensor
 | Fixed Temperature Heat Switches | Rate-of-Rise Heat Sensors
What they do | Trigger alarm when a set temperature threshold is reached | Trigger alarm when temperature rises rapidly over time
When to use | In stable environments where temperature doesn't fluctuate | In environments with hot or varying temps, to avoid false alarms from normal heat
Example | Activates if 68°C is reached in a storage room or office | Triggers if temp rises >7°C per minute in kitchens or boiler rooms
Complexity | Simple and easy to implement | More complex, requires more processing than a basic switch to measure how quickly the temperature changes over time.

## Slide 11: System inputs
Smoke Sensor
Used to detect
slow-burning fires

## Slide 12: System inputs
Smoke Sensor
Used to detect
slow-burning fires

## Slide 13: System inputs
Smoke Sensor
Used to detect
slow-burning fires

## Slide 14: System inputs
Smoke Sensor
Emitter
Photo Sensor
A light beam is sent from an emitter to a photo receiver across a space (sometimes several meters apart).
In normal conditions, the beam reaches the sensor uninterrupted.
When smoke enters, it blocks or scatters the beam, and the drop in received light triggers the alarm
Used to detect
slow-burning fires

## Slide 15: System inputs
Smoke Sensor
Emitter
Photo Sensor
A light beam is sent from an emitter to a photo receiver across a space (sometimes several meters apart).
In normal conditions, the beam reaches the sensor uninterrupted.
When smoke enters, it blocks or scatters the beam, and the drop in received light triggers the alarm
Used to detect
slow-burning fires
Alert Circuit

## Slide 16: System Outputs
Indicates normal and safe conditions
Red Light
Device Status
Green Light
Signals fire detection or system alert.
Displays the current state of the system (on/off)
Alarm
Activates sound to warn users of danger
Starts spraying water after a time delay to control fire
Exit Door
Water Pumps
Automatically opens for emergency evacuation
Helps ventilate smoke and heat from the area after pump control flames
Fan

## Slide 17: Ladder Diagram 03

## Slide 18: Sequence
System ON / Off
User presses Start / Stop push button
Then
Red light ON
Alarm ON
Exit door motor ON
Wait 5 seconds
If heat or smoke sensor on:
Water pumps ON
Wait another 5 seconds
Exhaust fans ON
Green light ON
Normal condition (no fire)
If fire is detected
(by any of the following):
Smoke detector
Heat sensor
Manual push button

## Slide 19: Ladder Diagram
Let’s play with buttons!
Here

## Slide 20: Our team
Thank You
Abdelhamed Ragheb
Aya Abdelfatah
Esraa Salem
Lamia Eslam
Rofaida Ahmed
Suzan Mohammed
Tasneem Ahmed